## Slide 1: Integrating low-temperature renewables in district heating and cooling systems
Focus on Belarus
February 3-4 2021
BELARUSIAN NATIONAL TECHNICAL UNIVERSITY
PROFESSOR V.A. SEDNIN and ALEXEI SEDNIN

## Slide 2
HISTORY OF THE DEVELOPMENT OF DISTRICT HEATING
IN THE REPUBLIC OF BELARUS
Start: early nineties of the twentieth century.
1990.
Developed district heating systems with the extraction factors (cogeneration) of over 50%
1994 – 2000
Decentralisation (extensive construction of gas-fired boiler houses, disconnected from district heating systems)
Widespread implementation of heat metering and automation systems
Start of use of pre-insulated heat pipes
2000 – 2010
Construction of small and medium-sized gas-fired CHPs
2005 – 2020
Construction of boiler houses using local fuel
Construction of several mini-CHPs using local fuels.

## Slide 3
Heat production
by category of energy producer
million gigacalories
BELSTAT
Utility condensing power plants
Utility district boiler houses
Utility CHPs
Boiler houses of organisations
CHPs and mini-CHPs of organisations

## Slide 4
million gigacalories
Heat consumption
including climatic factors
BELSTAT
Heat consumption
Heat consumption \including climatic factor

## Slide 5
Dynamics of end-use heat energy demand
million gigacalories
BELSTAT
Used by organisations
Energy delivered to the population

## Slide 6
Energy consumption from renewable energy sources in the Republic of Belarus
BELSTAT
7.2.1.1 Share of primary energy generation (production) from renewable energy sources in gross consumption of fuel and energy resources, %
Share of electrical energy generation from renewable energy sources in total generation of electrical energy, %
Share of generation of heat energy from renewable energy sources in total generation of heat energy, %
Emissions of pollutants into the atmospheric air from fuel combustion for heat and electricity generation, thousand tonnes
per capita, kg per person
per unit area, kg/km2
Emissions of pollutants into the atmospheric air from mobile sources, thousand tonnes
per capita, kg per person
per unit area, kg/km2
Greenhouse gas emissions in the energy sector, million tonnes CO2-equivalent per year
of which СО2

## Slide 7: Towards improving and developing district heating systems (Concept of the Development of District Heating in the Republic of Belarus to 2020)
Adopted in 2010.
Revised in 2017.
Amended in 2020 and extended to 2025.

## Slide 8
Strategic directions for the development of district heating:
- Improving efficiency and ensuring continuous development of district heating systems by applying modern technologies, using local fuel and energy resources, secondary energy resources and alternative energy sources;
- reliable, economic and secure supply of thermal energy to organisations and the population;
- maximising the use of combined heat and power generation;
- keeping the balance between the economic interests of energy supplying organisations (thermal energy suppliers) and consumers;
- ensuring an economically justified return on investment capital under the conditions of state regulation of heat tariffs;
- establishing an optimal management structure for heat supply processes;
- eliminating intermediaries in the supply of heat energy to consumers;
- improving regulations.

## Slide 9: Among the most representative solutions
the application of multi-rate district heating tariffs taking into account fuel taxes depending on their environmental properties;
increased use of alternative fuels in place of natural gas and oil (combustible refuse, biomass, solar energy, geothermal energy, secondary energy resources from industrial production, etc.).

## Slide 10: Structure of energy generation sources in Belarus after 2020
NPP
Q = const
To consumers
Network areas of the heating system
(Q = const)
Q = var
Q = var
Q = const
Q = const
Boiler house
Electric boilers in boiler houses
CHP electric boilers
CHP
Combined cycle (CCGT-CPP)
Steam turbine
CCGT-CPP
CPP
NPP
Isolated generating plant
W = var
W = var
W = var
W = const
W = const
W = const
Power grid
(W=const)
W = const
To consumers

## Slide 11
A scenario of the situation in the Belarusian energy system after
the commissioning of the BelNPP. Heating season
NPP
Surplus energy
Electrical energy consumption
[кэе]
[тэн]
[клок-стаячии]
NPP
mW
Time of day, hr

## Slide 12
A SCHEMATIC DIAGRAM FOR INTEGRATING AN ENERGY COMPLEX AND A HEAT-PUMP SYSTEM INTO A DISTRICT HEATING SYSTEM
CHP
ЗК (to clarify)
БА (to clarify)
Heat-pump system
БА (to clarify)
Main heating networks
Submain heating networks

## Slide 13
OPTIONS FOR INTEGRATING CUSTOMER TERMINALS INTO A DISTRICT HEATING SYSTEM: centralisation
thermal energy source
Consumer 5
Consumer 1
Consumer 4
Consumer 6
Consumer 3
Consumer 2
AT (to clarify)

## Slide 14
OPTIONS FOR INTEGRATING CUSTOMER TERMINALS INTO A DISTRICT HEATING SYSTEM: decentralisation
Thermal energy source
Consumer 1
Consumer 5
Consumer 4
Consumer 6
Consumer 3
Consumer 2
AT (to clarify)
AT (to clarify)
AT (to clarify)
AT (to clarify)
AT (to clarify)
AT (to clarify)
AT (to clarify)

## Slide 15
Structure of central heat supply station energy flows with energy complex and customer terminals, heat pump
Central heat supply station
energy complex
AT (to clarify)
TH
Q
Q
Q
Q
Qгвс
Qco
QTC
Qair flow
EЭС
EЭС

## Slide 16
A schematic diagram of a combined heat and power unit
Fuel
CCGT
Absorption heat pump
hot water storage tank
peak-reserve energy source
Со-Аh
Therm.
energy (130°С)
Therm.
energy
Fuel
Electricity
Therm.
energy
Therm.
energy
to the consumer

## Slide 17
Co-generation-based absorption heat-exchange (Co-ah) system - a type of district heating system using absorption heat converters
Return Water
50°C
130°C
70°C
Return water
Primary Heat Network
Supply water
Secondary Heat Network
Supply water
70°C
80°C
85°C
55°C
Q2
Q2
2
E
Qg
Qe
Qg+Qe
C
A
Return water
Return water
Return water
Return water
Supply water
Secondary Heat Network
Secondary Heat Network
Supply water
Supply water
Supply water
Primary Heat Network
68°C
130°C
70°C
50°C
50°C
70°C
25°C
25°C
130°C
Plate Heat Exchanger
Absorption Exchanger
1-Absorption heat pump 2-Water/water heat-exchanger
G-generator E-evaporator A-absorber C-condensor
Primary Heat Network
1
G

## Slide 18
A schematic diagram of a district heating peak-reserve energy source based on a combustion turbine unit
with a combined cycle gas turbine
Fuel
Air
Condensate
Flue gases
Heat recovery steam generator
Live steam
Heat extraction
Water to
storage tank
Fuel
Air
Water from
storage tank
Storage tank
wastewater treatment 25°С
industrial waste water 130°С
from the consumer
to the consumer
Boiler house
Со-Аh
return water
return water
Flue gases
peak-reserve energy source
combustion turbine unit 6x53 MW
Flue gases
Flue gases
Electricity
Electricity
Electricity
combustion turbine unit
Absorption heat pump
Heat recovery system

## Slide 19
Net present value as a function of
the cost of fuel (natural gas)
gas compressor unit with cogeneration
combustion turbine unit in a simple cycle
combustion turbine unit with cogeneration
gas compressor unit in a simple cycle
NPV [мая] USD
[Цои текцлика (га)] USD/[thou.] m3

## Slide 20
Thank you for your attention!